## Slide 1: UNIT-III: Fundamentals of Electrical Machines

## Slide 2: TRANSFORMER
Principle of Operation: Mutual inductance and mutual coupling phenomena in transformer
Construction
Working
Concept of Turns Ratio
Applications
Transformer on DC
Autotransformer
Instrument transformers

## Slide 3
In Brief, A transformer is a static electrical device that transfers electrical energy between two or more circuits through electromagnetic induction.

## Slide 7: TRANSFORMER SYMBOLS

## Slide 8: Principle of operation
It is based on principle of MUTUAL INDUCTION. According to which an e.m.f. is induced in a coil when current in the neighbouring coil changes.

## Slide 9: PRINCIPLE OF TRANSFORMER It works on the principle of Electromagnetic induction. The current flowing in the primary winding of the transformers creates a magnetic field, magnetic flux flows to the secondary side of the transformers, which induces EMF in the winding and current flows when the circuit is closed.
A varying current in one coil of the transformer produces a varying magnetic field, which in turn induces a varying electromotive force (emf) or "voltage" in a second coil.

## Slide 16
Notes: 16

## Slide 17: TRANSFORMER ON DC SUPPLY
What will happen if the Primary of a Transformer is Connected to D.C. Supply????

## Slide 23
Auto-Transformer
An Auto-transformer is an electrical transformer with only one winding.

## Slide 29: DC MACHINES
DC MOTOR
DC GENERATOR
Working principles
Classification
Starting of DC Machines
Speed control of DC Motor
Applications of dc motors

## Slide 31: Review of magnetism
31
The magnetic lines around a current carrying conductor leave from the N-pole and re-enter at the S-pole.
"Left Hand Rule" states that if you point the thumb of your left hand in the direction of the current, your fingers will point in the direction of the magnetic field.
Lines of flux define the magnetic field and are in the form of concentric circles around the wire.
The flow of electrical current in a conductor sets up concentric lines of magnetic flux around the conductor.

## Slide 32
Fleming’s left hand rule
Used to determine the direction of force acting on a current carrying conductor placed in a magnetic field .
The middle finger , the fore finger and thumb of the left hand are kept at right angles to one another .
The middle finger represent the direction of current
The fore finger represent the direction of magnetic field
The thumb will indicate the direction of force acting on the conductor .
This rule is used in motors.

## Slide 33
Fleming’s left hand rule

## Slide 34
Fleming’s left hand rule
Used to determine the direction of force acting on a current carrying conductor placed in a magnetic field .
The middle finger , the fore finger and thumb of the left hand are kept at right angles to one another .
The middle finger represent the direction of current
The fore finger represent the direction of magnetic field
The thumb will indicate the direction of force acting on the conductor .
This rule is used in motors.

## Slide 35
Fleming’s Right hand rule

## Slide 36: What are DC Machines?
Are DC generators that convert mechanical energy to DC electric energy.
Are DC motors that convert DC electric energy to mechanical energy.
DC machine can be used as a motor or as a generator.
DC Machine is most often used for a motor.
Notes: EMT 462 ELECTRICAL SYSTEM TECHNOLOGY
MMR
36

## Slide 37: DC MOTOR: INTRODUCTION
DC motors are found in many special industrial environments
  Motors drive many types of loads from fans and pumps to presses and conveyors
The major advantages of dc machines over generators are easy to control speed and torque regulation.
However, their application is limited to mills, mines and trains. As examples, trolleys and underground subway cars may use dc motors.
In the past, automobiles were equipped with dc dynamos to charge their batteries, but now dynamos are replaced by alternators.

## Slide 39: CONSTRUCTION OF DC MACHINES
DC motor stator
Rotor of a dc motor

## Slide 40: COMPONENTS OF DC MACHINE

## Slide 41: DC Machines Construction
41
DC machines, like other electromechanical energy conversion devices have
two sets of electrical
windings
  field windings - on stator
  amarture windings - on the rotor.
.

## Slide 42: DC Machines Construction
42
The stator of the dc motor has poles, which are excited by dc current to produce magnetic fields.
In the neutral zone, in the middle between the poles, commutating poles are placed to reduce sparking of the commutator. The commutating poles are supplied by dc current.
Compensating windings are mounted on the main poles. These short-circuited windings damp rotor oscillations.

## Slide 43: DC Machines Construction
43
The poles are mounted on an iron core that provides a closed magnetic circuit.
The motor housing supports the iron core, the brushes and the bearings.
The rotor has a ring-shaped laminated iron core with slots.
Coils with several turns are placed in the slots. The distance between the two legs of the coil is about 180 electric degrees.

## Slide 44: DC Machines Construction
44
The coils are connected in series through the commutator segments.
The ends of each coil are connected to a commutator segment.
The commutator consists of insulated copper segments mounted on an insulated tube.
Two brushes are pressed to the commutator to permit current flow.
The brushes are placed in the neutral zone, where the magnetic field is close to zero, to reduce arcing.
Notes: EMT 462 ELECTRICAL SYSTEM TECHNOLOGY
MMR
44

## Slide 45: DC Machines Construction
45
The commutator switches the current from one rotor coil to the adjacent coil,
The switching requires the interruption of the coil current.
The sudden interruption of an inductive current generates high voltages .
The high voltage produces flashover and arcing between the commutator segment and the brush.

## Slide 47: Principle of Operation
47
The generated voltage of a DC machines having (p) poles and (Z) conductors on the armature with (a) parallel path between brushes as below :
where K = pZ /(2πa) = machine constant
The mechanical torque which also equal to electromagnetic torque, is found as follows:
In the case of a generator, τm is the input mechanical torque, which is converted to electrical power. For the motor, τe is developed electromagnetic torque, which used to drive the mechanical load.

## Slide 48: Principle of Operation
48
ARMATURE winding are defined as the winding which a voltage is induced.
FIELD windings are defined as the windings that produce the main flux in the machines.
The magnetic field of the field winding is approximately sinusoidal, thus AC voltage is induced in the armature winding as the rotor turns under the magnetic field of stator.
The COMMUTATOR and BRUSH combination converts the AC generated voltages to DC.

## Slide 49: Principle of Operation
49
The induced or generated DC voltage (EA) appearing between the brushes is a function of the field current (IF) and the speed of rotation (ω) of the machine. This generated voltage is :
Where
K’ = voltage constant
ω = rotation per min
If the losses of the DC machine are neglected, the electrical power is equal to the mechanical power

## Slide 50: WORKING OF DC MOTOR
50

## Slide 51: Current in DC Motor
51

## Slide 52: Magnetic Field in DC Motor
52

## Slide 53: Force in DC Motor
53

## Slide 54: Types of DC Motors
Chap 2: DC Machines
54
DC motors are classified according to electrical connections of armature windings and field windings.
Armature windings: a winding which a voltage is induced
Field windings: a winding that produces the main flux in machines
Five major types of DC motors:-
    Separately excited DC motor
    Shunt DC motor
    Permanent Magnet DC motor
    Series DC motor
    Compounded DC motor
Notes: EMT 462 ELECTRICAL SYSTEM TECHNOLOGY
MMR
54

## Slide 55: Types of DC Machines
Self-excited DC machine: when a machine supplies its own excitation of the field windings. In this machine, residual magnetism must be present in the ferromagnetic circuit of the machine in order to start the self-excitation process.
Separately-excited DC machine: The field windings may be separately excited from an eternal DC source.
Shunt Machine: armature and field circuits are connected in parallel. Shunt generator can be separately-excited or self-excited.
Series Machine: armature and field circuits are connected in series.
Notes: 55

## Slide 56: Applications of DC Motors
Shunt Motor:
Blowers and fans
Centrifugal and reciprocating pumps
Lathe machines
Machine tools
Milling machines
Drilling machines

## Slide 57: Applications of DC Motors
Series Motor:
Cranes
Hoists , Elevators
Trolleys
Conveyors
Electric locomotives

## Slide 58: Applications of DC Motors
Cumulative compound Motor:
Rolling mills
Punches
Shears
Heavy planers
Elevators

## Slide 59
A magnetic field exists around
iron
copper
aluminium
moving charges

## Slide 60
Ans: d

## Slide 61
Which of the following is a vector quantity ?
Relative permeability
Magnetic field intensity
Flux density
Magnetic potential

## Slide 62
Ans: b

## Slide 63
The ratio of intensity of magnetisation to the magnetisation
force is known as
flux density
susceptibility
relative permeability
none of the above

## Slide 64
Ans: b

## Slide 65
The unit of relative permeability is
henry/metre
henry
henry/sq. m
it is dimensionless

## Slide 66
Ans: d

## Slide 67
Degaussing is the process of
removal of magnetic impurities
removing gases from the materials
remagnetising metallic parts
demagnetising metallic parts

## Slide 68
Ans: d

## Slide 69
Gilbert is a unit of
electromotive force
magnetomotive force
conductance
permittivity

## Slide 70
Ans: b

## Slide 71
Reciprocal of permeability is
reluctivity
susceptibility
permittivity
conductance

## Slide 72
Ans: a

## Slide 73
The commonly used material for shielding or screening magnetism is
copper
aluminium
soft iron
brass

## Slide 74
Ans: c

## Slide 75: DC Generators
Chap 2: DC Machines
75
DC generators are dc machines used as generator. There are five major types of dc generators, classified according to the manner in which their field flux is produced:
Separately excited generator: In separately excited generator, the field flux is derived from a separately power source independent of the generator itself.
Shunt generator: In a shunt generator, the field flux is derived by connecting the field circuit directly across the terminals of the generators.
Series generator: In a series generator, the field flux is produced by connecting the field circuit in series with the armature of the generator.
Cumulatively compounded generator: In a cumulatively compounded generator, both a shunt and series field is present, and their effects are additive.
Differentially compounded generator: In differentially compounded generator: In a differentially compounded generator, both a shunt and a series field are present, but their effects are subtractive.

## Slide 77: DC GENERATOR: Generation of Unidirectional Voltage
77
As the rotor is rotated at an angular velocity (ω), the armature flux linkage (Φ) change and a voltage eaa’ is induced between terminal a and a’. The expression for the voltage induced is given by Faraday’s Law
Two pole DC generator
Flux linkage of coil aa’; b) induced voltage;
c) rectified voltage

## Slide 78: Generation of Unidirectional Voltage
78
The internal generated voltage in the DC machines defined as:
Where EA = armature voltage
K = motor constant
= flux
= rotation per min

## Slide 79
Shunt Generators:
a. in electro plating
b. for battery recharging
c. as exciters for AC generators.
Applications of DC Generator
Series Generators :
A. As boosters
B. As lighting arc lamps

## Slide 80: Starting of DC motors
A starter is a device to start and accelerate a motor. A controller is a device to start the motor, control and reverse the speed of the DC motor and stop the motor. While starting the DC motor, it draws the heavy current which damages the motor.
The starter reduces the heavy current and protects the system from damage.
Need of Starters for DC Motors:
The dc motor has no back emf. At the starting of the motor, the armature current is controlled by the resistance of the circuit. The resistance of the armature is low, and when the full voltage is applied at the standstill condition of the motor, the armature current becomes very high which damage the parts of the motor.
Since at the time of starting the DC Motor, the starting current is very large. At the time of starting of all DC Motors, except for very small motors, an extra resistance must be connected in series with the armature. This extra resistance is added so that a safe value of the motor is maintained and to limit the starting current until the motor has attained its stable speed.

## Slide 81
According to the speed equation of a dc motor
N ∞ Eb/φ
∞ V- Ia Ra/ φ
Thus speed can be controlled by:
Flux control method: By Changing the flux by controlling the current through the field winding.
Armature control method: By Changing the armature resistance which in turn changes the voltage applied across the armature
Speed Control of DC motors

## Slide 82
Advantages:
It provides relatively smooth and easy control
Speed control above rated speed is possible
As the field winding resistance is high the field current is small. Power loss in the external resistance is small . Hence this method is economical
Disadvantages:
Flux can be increased only upto its rated value
High speed affects the commutation, motor operation becomes unstable
Flux Control Method

## Slide 83
Armature Voltage Control Method
The speed is directly proportional to the voltage applied across the armature .
Voltage across armature can be controlled by adding a variable resistance in series with the armature
Potential Divider Control
If the speed control from zero to the rated speed is required , by rheostatic method then the voltage across the armature can be varied by connecting rheostat in a potential divider arrangement .

## Slide 84
No-load speed of which of the following motor is highest?
Differentially compound motor
Cumulative compound motor
Series Motor
Shunt Motor

## Slide 85
Series Motor
Explanation:
At the time of starting, flux is very less in DC series motor.
So as we know the inverse relationship between speed
and flux i.e flux decrease when speed increase.
Therefore we never start DC series motor at no load.

## Slide 86
Which of the following load normally need starting torque
more than the rated torque?
Conveyors
Blowers
Centrifugal pump
Air compressor

## Slide 87
Conveyors Explanation:
Starting torque is also called the locked-rotor torque and the motor current at this point is referred to as the ‘locked rotor current. At this stage, the rotor reactance is higher than its resistance, as the rotor frequency is at its highest (equals the supply frequency).
Starting torque is the amount of torque required to
overcome the inertia of a standstill motor.
Conveyors require high starting torque because the material is placed before the starting of the Conveyors belt.
So obviously we require more torque to overcome the
load at the starting period.
Therefore conveyor required high starting torque and constant speed.
Series motor is suitable for conveyor belts operating in a particular region of its torque-speed characteristics.
In industries BLDC is used, as BLDC provides PWM
speed controlling method which is easier to vary the speed as well as with low maintains.

## Slide 88
Which of the following rule is used to determine the
direction of rotation of D.C motor?
Coloumb’s Law
Lenz’s Law
Fleming’s Right-hand Rule
Fleming’s Left-hand Rule

## Slide 89
Fleming’s left-hand rule.
Explanation:
When a current-carrying conductor such as a wire attached to a circuit moves placed in a magnetic field, an electric current is induced in the wire due to Faraday’s law of induction.
The right hand is held with the thumb, first finger and second finger mutually perpendicular to each other than
The thumb is pointed in the direction of the motion of the conductor relative to the magnetic field i.e direction of the force.
The forefinger is pointed in the direction of the magnetic field.
The middle finger represents the direction of the induced or generated current within the conductor.

## Slide 90
Which part of DC motor can sustain maximum
temperature rise?
Armature Winding
Field winding
Slip Ring
Commutator

## Slide 91
Commutator
Explanation:
The commutator is made up of copper segments.
This copper segment is insulated from each other with the help of mica.
Mica has a very high dielectric stress of about 1180
kV/cm and the next best is Diamond.
It can withstand high temperatures, up to 600 deg C.

## Slide 92
The ratio of starting torque to full load torque is least in
Differential Compound Motor
Shunt motor
Series Motor
Cumulative compound motor

## Slide 93
Differential Compound motor
Explanation:
In the differential compound, motor two field windings i.e shunt and series windings oppose each other.
This causes a reduction in flux and consequences
decrease in torque

## Slide 94
The efficiency of the DC motor at maximum power is
90%
100%
Around 80%
Less than 50%

## Slide 95
Less than 50% Explanation:
Why efficiency of D.C motor is below 50%
The DC motor develops maximum power when the Back
EMF is half the applied voltage is Eb = V/2.
Practically it is not possible to develop an exact 50% of maximum power because in that case, the current would be much beyond the rated current of the motor.
Some of the energy is wasted in the form of heat and other losses. Therefore motor efficiency is below 50%.

## Slide 96
In which of the following application DC series motor is used?
Centrifugal Pump
Motor Operation in DC and AC
Water pump drive
Starter for car

## Slide 97
Starter for car
Explanation:
In DC series motor Torque (Ta) increase as the Square of armature current (Ia) Ta 𝖺 Ia2.
So DC motor provides high starting torque which is
required to start a car.

## Slide 98
A three-point starter is suitable for
Shunt Motor
Series Motor
Shunt & Compound Motor
Shunt, Series, and compound motor

## Slide 99
Shunt & Compound motor Explanation:
3 point starters in DC Shunt and Compound machines
serve for the following purposes.
It limits the high starting current into the armature by having the resistance high at the time of starting and reducing it during the running conditions.
It also protects the motor from overload and under-
voltage conditions.

## Slide 100
Which DC motor has the least percentage increase in
Input current for the same percentage increase in torque?
Separately excited motor
Series motor
Shunt motor
Compound motor

## Slide 101
Answer 2. Series motor Explanation:
In DC series motor both field and armature windings carry the same current from source as both are connected in series.
Therefore torque is directly proportional to the product of current in field and armature windings.
For a given source current the torque produced is square of this current. So, even there is low current change, the torque change is great.

## Slide 102
By looking at which particular part of the motor we can
Identify a “DC motor”?
Shaft
Field winding
Commutator
Armature winding

## Slide 103
Commutator Explanation:
The commutator converts the alternating current generated in armature into the unidirectional current.
It is a mechanical rectifier, so the commutator collects
induced EMF or current developed in the armature.
In the DC motor, the commutator is used to alternate the magnetic field created by the DC current.
For AC motor the magnetic field is already alternated by the nature of the AC current.

## Slide 104
Counter EMF of the DC motor is
Less than the applied voltage
More than the applied voltage
Equal to the applied voltage
None of the above

## Slide 105
Less than the applied voltage Explanation:
According to DC motor equation,
Ia = (V – Eb)/Ra
⇒ V = Eb + IaRa

## Slide 106
If the back EMF of DC motor vanishes then
The motor continues to run
Motor will stop
Armature will burn
The motor continues to run in slow speed

## Slide 107
The armature will burn Explanation:
Explanation:
The presence of back emf makes the d.c. motor a self- regulating machine i.e., it makes the motor to draw as much armature current as is just sufficient to develop the torque required by the load.
Armature current is Ia = (V – Eb)/Ra
When the motor is running on no-load, small torque is required to overcome the friction and windage losses.
As Eb is zero the armature current will increases to a very high value, therefore a large amount of heat will be produced which may burn the armature winding.

## Slide 108
Why is the speed of DC shunt motor dependent on Back
EMF?
Because flux is proportional to the armature current
Because armature drop is negligible
Because Back EMF is equal to armature current
Because flux is constant in DC shunt motor

## Slide 109
Because flux is constant in DC shunt motor. Explanation:
In the case of DC motors Speed 𝖺 Back emf(Eb)/flux(φ).
The field winding is connected across the armature. The resistance offered by the field is constant so the current is constant. As current is constant flux also becomes
constant b the cause flux is directly proportional to current.
Therefore the speed of the DC shunt motor depends on
the back EMF.

## Slide 110: An induction motor or asynchronous motor is an AC electric motor in which the electric current in the rotor needed to produce torque is obtained by electromagnetic induction from the magnetic field of the stator winding
INDUCTION MOTORS

## Slide 111: Single Phase Induction Motor
111
The single-phase induction machine is the most frequently used motor for refrigerators, washing machines, clocks, drills, compressors, pumps, and so forth.
The single-phase motor stator has a laminated iron core with two windings arranged perpendicularly.
  One is the main and
  The other is the auxiliary winding or starting winding

## Slide 112: Construction of Single Phase Induction Motor
112

## Slide 113: Single Phase Induction Motor
*
This “single-phase” motors are truly two-phase machines.
The motor uses a squirrel cage rotor, which has a laminated iron core with slots.
Aluminum bars are molded on the slots and short-circuited at both ends with a ring.
Single-phase induction motor.

## Slide 114: Single Phase Induction Motor
*
Squirrel cage rotor

## Slide 115: Operating principle
*
115

## Slide 116: 7.6 Single Phase Induction Motor
*
116
The single-phase induction motor operation can be described by two methods:
  Double revolving field theory; and
  Cross-field theory.
Double revolving theory is perhaps the easier of the two explanations to understand
Learn the double revolving theory only

## Slide 117: Single Phase Induction Motor
*
117
Double revolving field theory
A single-phase ac current supplies the main winding that produces a pulsating magnetic field.
Mathematically, the pulsating field could be divided into two fields, which are rotating in opposite directions.
The interaction between the fields and the current induced in the rotor bars generates opposing torque

## Slide 118: Single Phase Induction Motor
118
The interaction between the fields and the current induced in the rotor bars generates opposing torque.
Under these conditions, with only the main field energized the motor will not start
However, if an external torque moves the motor in any direction, the motor will begin to rotate.
Single-phase motor main winding generates two rotating fields, which oppose and counter-balance one another.

## Slide 120: Three Phase Induction Motor

## Slide 123: Construction

## Slide 125
Advantages of Three-Phase Induction Motor: These motors are self-starting and use no capacitor, start winding, centrifugal switch or other starting device.
APPLICATIONS
Three-phase AC induction motors are widely used in industrial and Commercial applications.