## Slide 1: Basic concepts
Networks must be able to transfer data from one device to another with complete accuracy.
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 2: Types of Errors

## Slide 3: Single-bit error

## Slide 4
Single bit errors are the least likely type of errors in serial data transmission because the noise must have a very short duration which is very rare. However this kind of errors can happen in parallel transmission.
Example:
If data is sent at 1Mbps then each bit lasts only 1/1,000,000 sec. or 1 μs.
For a single-bit error to occur, the noise must have a duration of only 1 μs, which is very rare.

## Slide 5: Burst error

## Slide 7
The term burst error means that two or more bits in the data unit have changed from 1 to 0 or from 0 to 1.
Burst errors does not necessarily mean that the errors occur in consecutive bits, the length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 8
Burst error is most likely to happen in serial transmission since the duration of noise is normally longer than the duration of a bit.
The number of bits affected depends on the data rate and duration of noise.

## Slide 9: Error detection
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.

## Slide 10: Redundancy

## Slide 11: Four types of redundancy checks are used in data communications

## Slide 12: Vertical Redundancy Check VRC

## Slide 14
Performance
🢂It can detect burst errors only if the total number of errors is odd.

## Slide 15: Longitudinal Redundancy Check LRC

## Slide 16: Performance
🢂LCR increases the likelihood of detecting burst errors.
🢂If two bits in one data units are damaged and two bits in exactly the same positions in another data unit are also damaged, the LRC checker will not detect an error.

## Slide 18: Cyclic Redundancy Check CRC

## Slide 19: Cyclic Redundancy Check
Given a k-bit frame or message, the transmitter generates an n-bit sequence, known as a frame check sequence (FCS), so that the resulting frame, consisting of (k+n) bits, is exactly divisible by some predetermined number.
The receiver then divides the incoming frame by the same number and, if there is no remainder, assumes that there was no error.

## Slide 20
Binary Division

## Slide 21: Polynomial

## Slide 22: Polynomial and Divisor

## Slide 23: Standard Polynomials

## Slide 25: Checksum

## Slide 28: At the sender
The unit is divided into k sections, each of n
bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented and becomes the checksum.
The checksum is sent with the data

## Slide 29: At the receiver
The unit is divided into k sections, each of n
bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, they are rejected.

## Slide 30: Performance
🢂The checksum detects all errors involving an odd number of bits.
🢂It detects most errors involving an even number of bits.
🢂If one or more bits of a segment are damaged and the corresponding bit or bits of opposite value in a second segment are also damaged, the sums of those columns will not change and the receiver will not detect a problem.

## Slide 31: Error Correction
It can be handled in two ways:
receiver can have the sender retransmit the entire data unit.
The receiver can use an error-correcting code, which automatically corrects certain errors.

## Slide 32: Single-bit error correction
To correct an error, the receiver reverses the value of the altered bit. To do so, it must know which bit is in error.
Number of redundancy bits needed
Let data bits = m
Redundancy bits = r
Total message sent = m+r
The value of r must satisfy the following relation:
2r ≥ m+r+1

## Slide 33: Error Correction

## Slide 34: Hamming Code

## Slide 35: Hamming Code

## Slide 36: Hamming Code

## Slide 37: Example of Hamming Code

## Slide 38: Single-bit error

## Slide 39: Error Detection